## Slide 1
C
CRYODISPATCH
Predict. Dispatch. Prove.
A hospital cold-chain plant — not a temperature dashboard.
ELCIA Tech Summit 2026 · Electronics City
Sense → classify → move → verify → ticket
Notes: Open with the floor map live. This is a plant that acts.

## Slide 2
The gap is not monitoring
1
eVIN already watches ILRs
National immunization stock + temperature. We do not replace it.
2
e-BloodBank already counts bags
Inventory is solved. Floor-level evacuate-and-prove is not.
3
if (temp > 8) is not intelligence
Judges have seen that dashboard. The plant has to act first.

## Slide 3
Three apps. One brain. MQTT as a contract.
Simulator
Python · 24 assets
MQTT-shaped JSON
Ingest
Newton plant +
greedy dispatch
Command
Floor map, T_eq,
custody PDF
Staff
Accept · QR · reject
wrong vault
Live path is HTTP → plant. Dashboard never subscribes to a broker. An ESP32 can replace the sim on the same payload.
cryo/{site}/assets/{id}/telemetry · /status (retained) · /lwt → PROBE_DEAD

## Slide 4
Sensor death is not a hot vault
1
PROBE_DEAD
Last-will / logger silent
Ticket only. Do not move stock.
2
THERMAL_EXCURSION
T_eq headed through the band
Spoilage clock + MOVE + compressor ticket
3
BOTH
Blind and hot
Worst case — evacuate and re-instrument

## Slide 5
Newton for the box. Not ARIMA.
τ dT/dt + T = T_eq
T_eq = T_set + α_door·door + α_h·(1 − health)
t* = −τ ln((T_th − T_eq)/(T − T_eq))
Judges see T_eq jump while air is still legal. Demo τ is compressed (~2 min). Physics is the same.
Skip
ARIMA
if (temp > 8)
MKT as a release decision
FCM / APNs
MQTT as the only bus

## Slide 6
Ninety seconds. A judge holds the phone.
1
0–10s
Plant, not a chart
2
10–25s
Kill probe → ticket, no MOVE
3
25–40s
Compressor: T_eq up, air still legal
4
40–65s
Accept. Wrong-vault QR fails.
5
65–80s
Second vault cascades to V8
6
80–90s
Custody PDF + kWh hold vs move

## Slide 7
Bands we hardcode. Claims we refuse.
RBC 2–6°C · vaccines 2–8°C
Platelets 22±2°C · FFP ≤ −30°C
Freeze ≤0°C is critical on alum vaccines
Door-open ≠ discard
Quarantine. Never auto-scrap.
Not FDA-certified
Not NABH / WHO PQS
Not an eVIN replacement
MKT does not prove potency

## Slide 8
C
Closed loop. Hardware-ready.
When a vault fails we classify the fault, move the right units to the right door with the right nurse, prove custody with QR, and open a compressor ticket — while refusing to evacuate on a dead sensor.
ESP32 sketch in docs/firmware · MQTT schema in docs/mqtt-schema.md · Demo: docs/demo-script.md
CryoDispatch · ELCIA Tech Summit 2026